## Slide 1: ARM9 Interrupt latency measurement and Data storage for Analysis
Christian Wörz 747833
Sanjeev Kumarr Gopal 747763
27.06.2014
[1]
Team Project

## Slide 2: Task description
On chip interrupt latency measurement
Provide timestamp and metered result
Compensation / correction of the result
Transmit the values to a computer
Store values in a database
Implement queries, (WCET, time range)

## Slide 3: The Chip
Advanced Interrupt Controller (AIC):
8 priority interrupt level (nested interrupts)
Fast interrupt, including banked registers
Flexible configuration and interrupt vectoring
ATMEL AT91RM9200:
ARM9 32Bit controller
>1MIPS per MHz
RTC, PMC, USB, Ethernet, ..
16 Register + CPSR
[1]

## Slide 4: System Overview
[2,3,4]

## Slide 5: Hardware Abstraction Layer
Application independent of the hardware
Layering -> Information hiding
Limited by realtime constraints

## Slide 6: Interrupt handling

## Slide 7: Latency measurement ILMS
Example
Transmission calculation

## Slide 8: System limits and result correction
Result correction:
Estimate switching and serving time of the ISR
based on assembly instructions @1MIPS per MHz
Enabled and disabled depends use case
System limits:
Maximum around 25 Hz
One sporadic task measurable with next buffer

## Slide 9: Read Data from ARM Processor
Java-Simple-Serial-Connector (JSSC) is used for reading the data from ARM9 Processor.
Steps Involved:
    Open the port.
    Set the parameters (Baud rate, Data bits, Stop bits, Parity).
    Read bytes from serial port.
    Close the port.
Data Format:
    34 bytes of data in String format.
    The data consists of timestamp, Latency value and the unit.
    DD/MM/YYYY HH:MM:SS Value Unit\n
    eg: "24/05/2014 16:59:39 0000080460 us\n“
Notes: Data rate in bits per second is equal to the symbol rate in bauds.
The number of data bits in each character. 8 (for most kinds of data, as this size matches the size of a byte)
Parity is a method of detecting errors in transmission.
Stop bits sent at the end of every character allow the receiving signal hardware to detect the end of a character and to resynchronise with the character stream.

## Slide 10: Database Prerequisites
Database Selection:
    Oracle database 11g Express Edition is used.
    SQL Developer is used for connecting to the database.
Table Creation:
    The table consists of three fields (TIME, LATENCY, UNIT).
    The following query is used to create the table.
              create table sanjeev.latency
              (
              TIME TIMESTAMP,
              LATENCY NUMBER,
              UNIT VARCHAR2(25)
              );

## Slide 11: Adding values to Database
Field Separation:
  The string is separated by “spaces” in-between.
  String[] data = received_data.split(" ");
    data[0] + data[1] = timestamp
    data[2] = latency
    data[3] = unit (us)
Writing to Database:
  SQL Query.
"insert into sanjeev.latency values (TO_DATE('"
+ timestamp + "', 'dd/mm/yyyy hh24:mi:ss'),'"
+ Integer.parseInt(latency) + "','" + unit + "')";
  24/05/2014 16:59:39 0000080460 us
  24/05/2014 16:59:39
  0000080460
  us
  0000080460
  us

## Slide 12: GUI for Receiving Data
Swing is the primary Java GUI widget toolkit.
  Jbutton, Jlabel, JComboBox, JTextField, Jseparator are
  used.
Notes: Swing - part of Oracle's Java Foundation Classes (JFC) — an API for providing a graphical user interface (GUI) for Java programs

## Slide 13: Threading
Threading concept is used.
Object instance is created.
Receive Data Button
start()
End Button
stop()
public void start() {
if (thread == null) {
thread = new Thread(this);
thread.start();
}
}
public void stop() {
thread.stop();
thread = null;
}
public void run() {
while (thread != null) {
ReadData();
}
thread = null;
}

## Slide 14: GUI For History of Latency
  By Latency.
Search criteria:
  By Date (Format : DD-MM-YYYY).

## Slide 15: Integrated GUI
The Data Receiver GUI and the History GUI are integrated into one single GUI.

## Slide 16: Conclusion ILMS
Results:
Measurement was implemented on chip
Precise result of around 1µs (depends on the timer)
Further work:
Message buffering, handshaking
Configuration via the Database/Application
Sync of the RTC
Result plausibility check

## Slide 17: Conclusion Database Software
Results:
Data was successfully received and stored in the database.
A GUI is designed for storing and retrieving of the data to and from the data base.
Further work:
Flexible messages, timestamps and precision.
Search by time Criteria.
A web Application for retrieving of values.

## Slide 18
DEMO
Thank You!!!

## Slide 19: Sources
[1] http://de.farnell.com/atmel/at91rm9200-ek/kit-evaluation-fuer- at91rm9200/dp/1629536
[2] http://www.alldatasheet.com/datasheet-pdf/pdf/412638/SHARP/ GP2Y0D02YK0F.html
[3] http://image.ec21.com/image/arm97/oimg_GC01721389_CA01721724/ AT91RM9200_Development_Board.jpg
[4] http://wiki.ntb.ch/infoportal/_media/embedded_systems/abatron_bdi/ bdi2000.jpg